## Slide 1: MPICH.NT
Design of the Windows NT device

## Slide 2: Introduction
Port MPICH to NT quickly
Emulate the P4 device

## Slide 3: MPICH P4 device
P4
PIbsend(…)
PIbrecv(…)
PInprobe(…)
MPID
MPI
Channel

## Slide 4: MPICH NT device
MPID
MPI
Channel
Receive
Send
NT
NT_PIbrecv(...)
NT_PIbsend(...)

## Slide 5: NT device : Send
NT Send
TCP/IP
VIA
SHMEM
NT_PIbsend()
ShmemLockedQueue.Insert(...)
NT_ViSend(...)
SendBlocking(...)
MPID
MPI
Channel
Notes: NT_PIbsend(tag,buffer,length,to)
if [to].shm … else if [to].via … else …
This could have been done with a function pointer.
TCP – not thread safe.
SendBlocking(tag, sizeof(int))
SendBlocking(length, sizeof(int))
SendBlocking(buffer, length)
SHMEM – thread safe.
Insert(buffer,length,tag,from)
After 15K message size:
InsertSHP(buffer,length,tag,from,mutex,event)
Insert local buffer address into remote queue
Wait for event to be signalled that the remote process has read the local buffer
The mutex synchronizes head to head shp(rndv) messages
Note:
InsertSHP is my shared memory rendezvous. I get better performance if I start
the shmem rndv at 15K even though the channel rndv doesn’t start until 20K.
VIA – not thread safe
Send(tag,length,buffer)
Send(buffer) if needed

## Slide 6: NT device : Receive multi-threaded
NT Receive
MessageQueue
ShmemLockedQueue
ShmRecvThread
ViWorkerThread
CommPortWorkerThread
NT_PIbrecv(...)
FillThisBuffer(...)
GetBufferToFill(...)
SetElementEvent(...)
RemoveNextInsert(...)
VipCQWait(...)
GetQueuedCompletionStatus(...)
TCP/IP
VIA
SHMEM
MPID
MPI
Channel
Notes: MessageQueue:
BLOCKING
FillThisBuffer(tag,buffer,length,*from)
Check unexpected queue for tag. If found, copy data to buffer
else save buffer pointer in the queue and wait for event to be set
NON-BLOCKING
PostBufferForFilling(tag,buffer,length,*id)
Wait(id) or Test(id)
Very similar to ADI-3:
GetBufferToFill == ADI_Handle_pkt
SetElementEvent == ADI_Handle_data
TCP/IP thread
Read(tag, sizeof(int))
Read(length, sizeof(int))
GetBufferToFill(…)
Read(buffer, length)
SetElementEvent(…)
VIA thread
VipRecvDone(…)
Copy tag,length into message
GetBufferToFill(…)
Copy data into buffer
SetElementEvent(…)
SHMEM thread
Wait for the next message in the shmem queue
Use the tag, length, and from fields and call GetBufferToFill(…)
Copy data into buffer
SetElementEvent(…)

## Slide 7: NT device : Receive “single” threaded
MessageQueue
Poll
SHMEM
VIA
CommPortWorkerThread
NT_PIbrecv(...)
FillThisBuffer(...)
GetBufferToFill(...)
SetElementEvent(...)
RemoveNextInsert(...)
ViWorkerThread(...)
GetQueuedCompletionStatus(...)
MPID
MPI
Channel
NT Receive
TCP/IP
PollShmemAndViQueues(...)
Notes: FillThisBuffer(tag,buffer,length,*from)
Check unexpected queue for tag
If found, copy data to buffer
Else save buffer pointer in the queue
This time instead of waiting for the event to be set,
call PollShmemAndViQueues to advance the progress
of messages until the event is set.
The Poll function calls the non-blocking versions of ViWorkerThread and RemoveNextInsert

## Slide 8: NT device : MessageQueue
Retrieving a buffer from the message queue:
void* GetBufferToFill( int tag, int length, int from, MsgQueueElement **ppElement )
bool SetElementEvent( MsgQueueElement *pElement )
Supplying a buffer to be filled by the message queue:
bool FillThisBuffer( int tag, void *buffer, int *length, int *from )
bool PostBufferForFilling( int tag, void *buffer, int length, int *pID )
bool Wait( int *pID )
bool Test( int *pID )
Miscellaneous:
bool Available( int tag, int &from )
void SetProgressFunction( void (*ProgressPollFunction)() )
Notes: Available is included to provide the Probe capability.
Available is a terrible function. Don’t use it. Available doesn’t return true until there is a message buffer in the queue. This guarantees that the message will be copied into a temporary buffer.

## Slide 9: NT device: ShmemLockedQueue
Single reader / Multiple writer
Inserting a buffer into the shared memory queue:
bool Insert( unsigned char *buffer, unsigned int length, int tag, int from );
Supplying a buffer to be filled by the shared memory queue:
bool RemoveNext( unsigned char *buffer, unsigned int *length, int *tag, int *from );
Removing the next message directly into a buffer supplied by a message queue:
bool RemoveNextInsert( MessageQueue *pMsgQueue, bool bBlocking = true );
Miscellaneous:
void SetProgressFunction( void (*ProgressPollFunction)() );

## Slide 10: ShmemLockedQueue
Memory layout with two messages in the queue:
state tag from length next offset
Message header
m_plQMutex
m_plQEmptyEvent
m_plMsgAvailableTrigger
m_pBase
m_pBottom
head tail
m_pEnd
m_hMsgAvailableEvent
Notes: m_plQEmptyEvent and m_plMsgAvailableTrigger are redundant but necessary. You could determine that the queue is not empty if there is a message available or you could determine that there is a message available when the queue is not empty. I supplied a separate location for the message available trigger because I wanted to have the option of using either a shared memory location, m_plMsgAvailableTrigger, or an OS event object, m_hMsgAvailableEvent, to signal when a message is available. The user determines this at runtime with the MPICH_USE_POLLING environment variable.
The queue is empty when the head offset is set to zero. This happens when the head catches up with the tail. The tail must always be greater than the head. This means that the tail does not wrap around the end. When a message is to be inserted that would cause the tail offset to go beyond m_pEnd, the queue blocks or polls until the queue is empty and then inserts it at the beginning. This solution was chosen for simplicity, not because it is the right thing to do.
The state of a message can be:
SHMEM_Q_READ – the message has been read or the space has never been used
SHMEM_Q_BEING_WRITTEN – the space is allocated and being written to
SHMEM_Q_AVAIL_FOR_READ – the message has been written and is ready to be read
SHMEM_Q_SHP_AVAIL_FOR_READ – the shp message has been written and is ready to be read
SHMEM_Q_BEING_READ – the message is being read
Fully thread safe.

## Slide 11: ProcTable : g_pProcTable[nproc]
// Structure accessed by completion port or via thread to store the current message
struct NT_Message
{
int tag;
int length;
void *buffer;
int nRemaining;
DWORD nRead;
OVERLAPPED ovl;
MessageQueue::MsgQueueElement *pElement;
int state; // NT_MSG_READING_TAG, NT_MSG_READING_LENGTH, NT_MSG_READING_BUFFER
};
struct NT_Tcp_shm_ProcEntry
{
SOCKET sock; // Communication socket
WSAEVENT sock_event; // Communication socket event
NT_Message msg; // Current working message for sockets or via
VI_Info vinfo; // VIA connection information
int shm; // FALSE(0) or TRUE(1) if this host can be reached through shared memory
int via; // FALSE(0) or TRUE(1) if this host can be reached through VI
int listen_port; // Port where thread is listening for connections
int control_port; // Port where thread is listening for control message connections
// Description of process
long pid; // process id
char host[NT_HOSTNAME_LEN]; // host where process resides
char exename[NT_EXENAME_LEN]; // command line launched on the node
HANDLE hValidDataEvent; // Event signalling the data in this structure is valid
// This does not include sock and sock_event
};
Notes: The NT_Message entry is like a single, static, receive only request. The socket and via methods use it to store information as each message arrives. It is necessary to maintain state between partial message arrival events.

## Slide 12: Send Call Tree
MPI_Send
MPID_SendDatatype
(MPID_PackMessage)
MPID_SendContig
MPID_CH_Eagerb_send_short
MPID_SendControlBlock
NT_PISend
NT_ShmSend
Insert or InsertSHP
NT_ViSend
ViSendFirstPacket –
tag,length,buffer
ViSendMsg
SendBlocking – tag
SendBlocking – length
SendBlocking - buffer
MPID_CH_Eagerb_send
MPID_SendControlBlock
NT_PISend
NT_PISend
MPID_NT_Rndvn_send
MPID_NT_Rndvn_isend
MPID_SendControlBlock
NT_PISend
Wait
CheckDevice

## Slide 13: Receive Call Tree
MPI_Recv
MPID_RecvDatatype
MPID_IRecvDatatype
MPID_IrecvContig
MPID_Search_unexpected_queue_and_post
MPID_Search_unexpected_queue
MPID_Enqueue
MPID_RecvComplete
check device
non-blocking
MPID_CH_Check_incoming
PInprobe = NT_Pinprobe
blocking
MPID_RecvAnyControl = PIbrecv = NT_Pibrecv
msgQ.PostBufferForFilling
msgQ.Wait
Notes: The NT device uses the blocking CheckDevice function. I tried the non-blocking option and the performance went down. I believe this is because of the probe function. I don’t like it because it forces the method to copy the message into a temporary buffer. Probe cannot return true until a message has arrived and a message cannot arrive unless there is a buffer to store it in.

## Slide 14: Limitations
MessageQueue has no concept of Datatypes, only contiguous buffers.
Blocking, single threaded sends.
Large buffers are completely filled before any unpacking is done.
Notes: It would be nice to have a non-blocking ADI_Handle_data() call that informs the device how much of the buffer has been received by the method. This way in a multithreaded device, the method could be receiving the last part of a message while the device is unpacking the first part of the message.
I would like the device to poll a method. Then the method starts to receive the message and determines that it is a large message. It then passes the work on to another thread and tells the device to stop polling. Then the thread periodically updates the device informing it of its current position until the message is completely received. With this information, the device can unpack the received part of the message while the method is receiving the rest of the message in parallel, in the other thread.